;Codes for Distributive law using AVR Assembly language.
;Distributive las is expressed by X.(Y+Z) = X.Y+X.Z
;LHS = X.(Y+Z), RHS = X.Y+X.Z

.include "/home/administrator/m328Pdef.inc"

ldi r17, 0b11000111	;identifying input pins 11,12,13 for inputs X, Y, Z
out DDRB,r17	;declaring pins as input
ldi r17, 0b00111001 ;

out PORTB,r17	;activating internal pullup for pins 11,12,13 and assigning pin 8 for output for LHS in PORTB
in r17,PINB

ldi r16, 0b00000100	;identifying output pin 2 and assignin pin 2 for RHS in PORTD
out DDRD,r16	;declaring pins as output

;Assigning six registers; 3 forLHS and 3 for RHS
;Copying data bits from input register r17 to six registers assigned for LHS and RHS

mov r18,r17	; for X of LHS
mov r19,r17	; for Y of LHS
mov r20,r17	; for Z of LHS

mov r21,r17	; for X of RHS
mov r22,r17	; for Y of RHS
mov r23,r17	; for Z of RHS

; For LHS

; to shift X to 1st cell of R18

lsr r18
lsr r18
lsr r18	; this is input X; 1st cell of R18

; to shift Y to 1st cell of R19
lsr r19
lsr r19
lsr r19
lsr r19	; this is input Y; 1st cell of R19

; to shift Z to 1st cell of R20
lsr r20
lsr r20
lsr r20
lsr r20
lsr r20	; this is input Z; 1st cell of R20

; performing operation for LHS= = X.(Y+Z)
or r19,r20
and r18,r19

out PORTB,r18	;writing output to pin 8 for LHS= = X.(Y+Z)

; For RHS

lsr r21 ; this is equal to input X
mov r24,r21

lsr r22
lsr r22; this is equal to Y

lsr r23
lsr r23
lsr r23	;this is equal to Z

; performing operation for RHS= = X.Y+X.Z
and r21,r22
and r24,r23
or r21,r24

out PORTD,r21	;writing output to pin 2 for RHS= = X.Y+X.Z

Start:
rjmp Start